## Slide 1: Geo-Routing Beaconless routing – Contention-based
By hungtt28

## Slide 2: Contents
Overview
Beaconless Routing – Contention-based (2003)
Beaconless Forwarder Planarization (2008)
Alpha-shape boundary (1980s - 2009)
Rotational Sweep Algorithm (2012)
ALBA-R (2014)

## Slide 3: Overview
Neighborhood-based
  Each node must know their 1-hop neighbor’s position
  Next hop decision is computed locally
  GPSR, BoundHole, …
HELLO message
  Construct NeighborTable
Broadcast position
Request
Send back position

## Slide 4: Overview
Hello message scheme
  Request on routing
  Broadcast periodically
Advantages
Disadvantages
  Need more energy for broadcast position information
  Locally computation
  Out of date NeighborTable

## Slide 5: Beaconless Routing
Beaconless
  Don’t use NeighborTable, each neighbor decides to be nexthop.
  Delay function
  “A novel position-based and beacon-less routing algorithm for mobile ad-hoc networks” - 2003
forwarder
candidate
Broadcast message forwarded

## Slide 6: Beaconless Routing
Basic mode
Backup mode / Recovery mode
  If no further forwarding
  Request neighbor’s position
  Clockwise-relaying
A
P
B
C
forwarder
drop
forward

## Slide 7: Beaconless Routing
Advantages
  No Hello message, no NeighborTable
Disadvantages
  Duplicate packet
  Inefficient in Backup mode

## Slide 8: Contention-based
Improve Beaconless
  Use RTS/CTS scheme
    RTS – Request to Send
    CTS – Clear to Seed
  Scheme
    Forwarder broadcast RTS
    Candidate compute delay function
    SetTimer to reply CTS
    If timer expired candidate send CTS
    If candidate receive CTS from other candidate then discard the timer
    Forwarder receive CTS, forward DATA to nexthop
  “MACA - A New Channel Access Method for Packet Radio” – 1990
  IEEE 802.11
forwarder
candidate
Broadcast RTS

## Slide 9: Contention-based
Delay function
  “the advance” – to compute delay function
    Distance to destination
    Angle of candidate and forwarder with destination
    … (depend on variant algorithm)
  Require
    Current position
    Destination position
    Forwarder position
    … (depend on algorithm)
Add_delay = Max_delay * “the advance”

## Slide 10: Contention-based
Position-based
  Like Greedy
Problem – stuck node
  Recovery mode – face routing
A
P
B
C
C
forwarder
nexthop
D
discard
CTS
CTS discarded

## Slide 11: Beaconless Forwarder Planarization
BFP (2008)
  Beaconless recovery
    Use RTS/CTS scheme to construct planar graph
    Locally select next hop

## Slide 12: Alpha-shape boundary
Alpha-shape – planar graph
  Rolling ball

## Slide 13: Rotational Sweep Algorithm
Rotational Sweep
  Sweep Circle – like rolling ball
  Twisting triangle
Advantages
  Beaconless totally
  Compute alpha-boundary on candidate

## Slide 14: Rotational Sweep Algorithm
Sweep Circle
  Delay function

## Slide 15: ALBA-R
Routing
  Contention-based
Load balancing
  Queue priority index (QPI)
  Geographic priority index (GPI)
  Rainbow table

## Slide 16: THANK YOU